## Slide 1
Chapter 3: Wave-mode separation in the continuous wavelet
domain using combined translational and rotational data
Vertical component
P waves
Notes: Hello, my name is Ohad, and this talk is about wave-mode separation of multicomponent seismic data.
We use a polarization filtering scheme in the the continuous wavelet domain to carry out this wave mode separation.
An example of what I mean by wave mode separation can be seen in this vertical geophone receiver gather:
here is a wave mode that obscures our desired P-wave reflections.
You can see that is has been removed here, and the P-wave reflections are now visible.

## Slide 2: Current state of the art
Data components:
Hydrophone
Vertical
Radial
Transverse
“Coherent noise” /
“Source generated noise”
S-waves
Wave modes:
Surface waves
“ground roll”
“Vz noise”
P-waves

## Slide 3: Wave-mode selectivity using translational + rotational data
Data components:
Hydrophone
Vertical
Radial
Transverse
Yaw
Roll
Pitch
…
Wave modes:
P-waves
S-waves
Rayleigh
Love
….

## Slide 4: Agenda
Current coherent noise removal methods

## Slide 5: Agenda
Current coherent noise removal methods
Polarization template matching
  Continuous Wavelet Transform (CWT)
  Singular Value Decomposition (SVD)

## Slide 6: Agenda
Current coherent noise removal methods
Polarization template matching
  Continuous Wavelet Transform (CWT)
  Singular Value Decomposition (SVD)
Kettleman six-component survey

## Slide 7: Agenda
Current coherent noise removal methods
Polarization template matching
  Continuous Wavelet Transform (CWT)
  Singular Value Decomposition (SVD)
Kettleman six-component survey
Polarization-based wave mode separation

## Slide 8: Coherent Noise
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Waves generated by the seismic source that do not contain information about the deep subsurface
Typically surface waves
Much stronger than the P-wave reflection data

## Slide 9: Ground roll / Rayleigh / Surface waves
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation

## Slide 10: Ground roll / Rayleigh / Surface waves
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Data courtesy of Shell

## Slide 11: Ground roll / Rayleigh / Surface waves
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Data courtesy of Shell

## Slide 12: Ground roll suppression: Mute
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Data courtesy of Shell

## Slide 13: Ground roll suppression with F-K
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Receivers spaced at 2m intervals
Courtesy of Gustavo Alves

## Slide 14: Ground roll suppression with F-K
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Receivers spaced at 8m intervals
Courtesy of Gustavo Alves

## Slide 15: Ground roll suppression with polarization analysis
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Multicomponent data (2C or 3C geophone)
Analysis of signal attributes of each multicomponent trace
Threshholding based on signal attributes to identify and separate noise from data

## Slide 16: Ground roll suppression with polarization analysis
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Multicomponent data (2C or 3C geophone)
Analysis of signal attributes of each multicomponent trace
Threshholding based on signal attributes to identify and separate noise from data
Not applicable to single component data

## Slide 17: Ground roll suppression with polarization analysis
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Multicomponent data (2C or 3C geophone)
Analysis of signal attributes of each multicomponent trace
Threshholding based on signal attributes to identify and separate noise from data
Can operate on spatially aliased data (3D surveys)
Insensitive to statics

## Slide 18: Ground roll suppression with polarization analysis
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Multicomponent data (2C or 3C geophone)
Analysis of signal attributes of each multicomponent trace
Threshholding based on signal attributes to identify and separate noise from data
Need to have some prior model of data or noise signal attributes

## Slide 19: Ground roll suppression with polarization analysis
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vidale, 1986: Eigenvalue decomposition of covariance matrix of analytic signal
Kendall et al., 2005: First polarization vector from singular value decomposition of data covariance matrix after low-pass filter
de Meersman et al., 2006: Similar to Kendall et al., but with better noise weighting
Diallo et al. 2006: analytic signal of data after continuous wavelet transform

## Slide 20: Ground roll suppression with polarization analysis
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Diallo et al., 2006

## Slide 21: Frequency-dependent polarization template matching
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Extract multiple attributes of input multicomponent signal
Insensitive to spatial aliasing
Frequency is an attribute
Data comprise translations and rotations
No prior model for noise. Noise model is learned directly from the data.

## Slide 22: Agenda
Current coherent noise removal methods
Polarization template matching
  Continuous Wavelet Transform (CWT)
  Singular Value Decomposition (SVD)
Kettleman six-component survey
Polarization-based wave mode separation

## Slide 23: Singular Value Decomposition (SVD)
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation

## Slide 24: Singular Value Decomposition (SVD)
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Scaled singular vectors

## Slide 25: Singular Value Decomposition (SVD)
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Polarization vectors

## Slide 26: Singular Value Decomposition (SVD)
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Data1 |  | Comp 1 | Comp 2
 | Sample 1 | 1 | 0
 | Sample 2 | -0.2 | 0
Data2 |  |  | 
 | Sample 1 | 0 | 0.2
 | Sample 2 | 0 | 0.6
Data3 |  |  | 
 | Sample 1 | 1 | 0.2
 | Sample 2 | -0.2 | 0.6
Polarization vectors

## Slide 27: Singular Value Decomposition (SVD)
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Data1 |  | Comp 1 | Comp 2
 | Sample 1 | 1 | 0
 | Sample 2 | -0.2 | 0
Data2 |  |  | 
 | Sample 1 | 0 | 0.2
 | Sample 2 | 0 | 0.6
Data3 |  |  | 
 | Sample 1 | 1 | 0.2
 | Sample 2 | -0.2 | 0.6
Polarization vectors

## Slide 28: Singular Value Decomposition (SVD)
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Data1 |  | Comp 1 | Comp 2
 | Sample 1 | 1 | 0
 | Sample 2 | -0.2 | 0
Data2 |  |  | 
 | Sample 1 | 0 | 0.2
 | Sample 2 | 0 | 0.6
Data3 |  |  | 
 | Sample 1 | 1 | 0.2
 | Sample 2 | -0.2 | 0.6
Polarization vectors

## Slide 29: Continuous Wavelet Transform
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
data
mother wavelet (Morlet)
daughter wavelet
dilation
time delay

## Slide 30: Continuous Wavelet Transform
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
data
mother wavelet (Morlet)
daughter wavelet
dilation
time delay

## Slide 31: Continuous Wavelet Transform
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
64
16
32
8
2
4
1

## Slide 32: Agenda
Current coherent noise removal methods
Polarization template matching
  Continuous Wavelet Transform (CWT)
  Singular Value Decomposition (SVD)
Kettleman six-component survey
Polarization-based wave mode separation

## Slide 33: Chevron’s six-component Kettleman survey
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation

## Slide 34: Chevron’s six-component Kettleman survey
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
1 survey line
Maximum offset = 1600 m
3C MEMS accelerometers at 2 m intervals
3C electrokinetic rotation sensors
4 different source types:
  Accelerated weight-drop
  Vibroseis
  Dynamite at depth = 25 m
  Dynamite at depth = 50 m

## Slide 35
Vertical
Radial
Transverse
Yaw
Roll
Pitch
Accelerated weight-drop source
Shot interval 6.25 m
Data courtesy of Chevron
Notes: AWD, clip=93%

## Slide 36
Vertical
Radial
Transverse
Yaw
Roll
Pitch
Vibroseis source
Shot interval 25 m
Data courtesy of Chevron
Notes: Vibroseis, clip=93%

## Slide 37
Vertical
Radial
Transverse
Yaw
Roll
Pitch
Dynamite source at depth = 25 m
Shot interval 25 m
Data courtesy of Chevron
Notes: Dynamite 25, clip=93%

## Slide 38
Vertical
Radial
Transverse
Yaw
Roll
Pitch
Dynamite source at depth = 50 m
Shot interval 25 m
Data courtesy of Chevron
Notes: Dynamite 50, clip=93%

## Slide 39: Rotations from geophone differencing on a free surface
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Pitch
r-sensor
Pitch
geo-diff
Dynamite source
d
1
2
Data courtesy of Chevron

## Slide 40: Rotations from geophone differencing on a free surface
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Pitch
r-sensor
Pitch
geo-diff
Dynamite source
3 components:
Vertical
Radial
Pitch
Data courtesy of Chevron

## Slide 41: Vibroseis source after NMO
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch
Data courtesy of Chevron

## Slide 42: Dynamite source at depth=25m after NMO
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch
Data courtesy of Chevron

## Slide 43: Dynamite source at depth=50m after NMO
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch
Data courtesy of Chevron

## Slide 44: Objectives
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch
Separate undesired wave modes from all data components
Insensitive to spatial aliasing
Does not rely on an a priori model of the noise
Data courtesy of Chevron

## Slide 45: Attributes that distinguish between wave modes
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch
Data courtesy of Chevron
Rayleigh wave appearance on each component
Rayleigh wave frequency
Incorporate a time-frequency dependence into polarization analysis
Polarization in the continuous wavelet domain
Learn noise polarization from the data

## Slide 46: Agenda
Current coherent noise removal methods
Polarization template matching
  Continuous Wavelet Transform (CWT)
  Singular Value Decomposition (SVD)
Kettleman six-component survey
Polarization-based wave mode separation

## Slide 47: Dynamite source at 50 m depth before removal of shear-induced wave
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 48: Dynamite source at 50 m depth after removal of shear-induced wave
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 49: 3C data in the continuous wavelet domain
Vertical
Radial
Pitch
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
CWT

## Slide 50: 3C data in the continuous wavelet domain
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
component
frequency
time

## Slide 51: CWT polarization
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
P-wave CWT
S-wave CWT
Singular value decomposition
Scaled singular vectors =
polarizations
1st
3rd
2nd

## Slide 52: CWT polarization
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
S-wave CWT
Scaled singular vectors =
polarizations
1st
Vz
Vx
Ry

## Slide 53: CWT polarization
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
S-wave polarization
P-wave polarization
S-wave CWT
P-wave CWT

## Slide 54: Polarization template
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
S-wave polarization template
Vz
Vx
Ry
1
0
weight

## Slide 55: Polarization template
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Some other arrival’s polarization
Vz
Vx
Ry
1
0
weight

## Slide 56: Weighting function
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation

## Slide 57: Continuous wavelet domain polarization filtering flow
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
CWT
SVD
CWT+SVD
CWT-1
polarization template
Weighting function

## Slide 58: Dynamite source at 50 m depth before removal of shear-induced wave
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 59: Dynamite source at 50 m depth after removal of shear-induced wave
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 60: Polarization filter vs frequency filter
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Input data
Polarization filter
High-pass filter

## Slide 61: Dynamite source at 25 m depth before removal of shear-induced wave
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 62: Dynamite source at 25 m depth after removal of shear-induced wave
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 63: Vibroseis source before removal of Rayleigh waves
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 64: Vibroseis source after removal of Rayleigh waves
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 65: Vibroseis source before removal of Rayleigh waves
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical

## Slide 66: Vibroseis source after removal of Rayleigh waves
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical

## Slide 67: Summary
Frequency-dependent polarization filtering using CWT and SVD
Matching wavelet-domain polarization template of an undesired wave-mode
Multicomponent translational + rotational field data
No spatial sampling requirement
Assumption of stationarity of undesired wave-mode

## Slide 68: Summary
Frequency-dependent polarization filtering using CWT and SVD
Matching wavelet-domain polarization template of an undesired wave-mode
Multicomponent translational + rotational field data
No spatial sampling requirement
Assumption of stationarity of undesired wave-mode
Chapter 4: Automatic wave-mode identification with machine learning

## Slide 69: Machine-learning classification at station 337
Manual wave-mode identification / Support Vector Machines / Automatic wave-mode identification
Training: Class 1=
Slow ground roll
Training: Class 1=
Fast ground roll
Training: Class 1=
Slow+fast ground roll
Class 1
Class 0
Class 1
Class 0
Class 1
Class 0
Data courtesy of Chevron

## Slide 70
Acknowledgements
Fred Herkenhoff and Ranjan Dash (Chevron)
Robert Brune (Geokinetics)
Everhard Muyzert (Schlumberger)
Notes: Hello, my name is Ohad, and this talk is about wave-mode separation of multicomponent seismic data.
We use a polarization filtering scheme in the the continuous wavelet domain to carry out this wave mode separation.
An example of what I mean by wave mode separation can be seen in this vertical geophone receiver gather:
here is a wave mode that obscures our desired P-wave reflections.
You can see that is has been removed here, and the P-wave reflections are now visible.

## Slide 71: Spare slides

## Slide 72: Comparison of weighting function with different components
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
C1
C2
C3
Cone

## Slide 73: Comparison of weighting function with different components
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Six components in Kettleman dataset:
Vertical
Radial
Transverse
Yaw
Roll
Pitch

## Slide 74: Comparison of weighting function with different components
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Compare filtering using:
Vertical
Radial
Transverse
+ Pitch
Vertical
Radial
Transverse
vs

## Slide 75: Comparison of weighting function with different components
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
C1
C2
C3

## Slide 76: Comparison of weighting function with different components
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
C3
C1
C2

## Slide 77: Comparison of weighting function with different components
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
C1
C2
C3
Slice

## Slide 78: Comparison of weighting function with different components
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
C1
C2
C3
Wedge

## Slide 79: Comparison of weighting function with different components
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
C1
C2
C3
Cone

## Slide 80: Comparison of weighting function with different components
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
C1
C2
Cone
C4

## Slide 81: Comparison of weighting function with different components
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Compare filtering using:
Vertical
Radial
Pitch
Vertical
Radial
Transverse
vs

## Slide 82: Transverse vs Pitch component, dynamite 25 m
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Transverse

## Slide 83: Transverse vs Pitch component, dynamite 25 m
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 84: Before removal of shear-induced wave, dynamite 25 m
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Transverse
Pitch

## Slide 85: After removal of shear-induced wave with vertical, radial, transverse
Transverse
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 86: After removal of shear-induced wave with vertical, radial, pitch
Pitch
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Transverse

## Slide 87: Before removal of slow ground roll, vibroseis
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Transverse
Pitch

## Slide 88: After removal of slow ground roll with vertical, radial, transverse
Transverse
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 89: After removal of slow ground roll with vertical, radial, pitch
Pitch
Transverse
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial

## Slide 90: Before removal of shear-induced wave, dynamite 50 m
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Transverse
Pitch

## Slide 91: After removal of shear-induced wave with vertical, radial, transverse
Transverse
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 92: After removal of shear-induced wave with vertical, radial, pitch
Transverse
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Vertical
Radial
Pitch

## Slide 93: Ground roll suppression with Stack-Array
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
(Morse and Hildebrandt, 1989)

## Slide 94: Ground roll suppression with Stack-Array
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
(Morse and Hildebrandt, 1989)

## Slide 95: Ground roll suppression with Stack-Array
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
(Morse and Hildebrandt, 1989)
Topography (Statics correction)
Assumption of surface wave velocity
Large scale 3D acquisition?
Acquisition design focused on noise suppression

## Slide 96: Vz noise in ocean bottom node data
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation

## Slide 97: Upgoing and downgoing wavefields
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
(M. Wong, 2014)
Upgoing
Downgoing

## Slide 98: Upgoing and downgoing wavefields
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
(M. Wong, 2014)
Upgoing
Downgoing
PZ summation:
Combine Hydrophone and vertical geophone to separate upgoing data from downgoing data

## Slide 99: Vz noise in ocean bottom node data
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Hydrophone
Vertical with Vz noise
(Zhou et al., 2011)

## Slide 100: Vz noise in ocean bottom node data
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Hydrophone
Vertical with Vz noise
(Zhou et al., 2011)
P wave
S wave

## Slide 101: Vz noise suppression with match filtering
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Hydrophone
Vertical with Vz noise
(Zhou et al., 2011)

## Slide 102: Vz noise suppression with match filtering
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Hydrophone
Vertical with Vz noise
Vertical after Vz noise suppression
(Zhou et al., 2011)

## Slide 103: Vz noise suppression with match filtering
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
Hydrophone
(Zhou et al., 2011)
Extension of the data dimensions to a domain where noise is separable from data
Requires an input model of “clean” data
Spatial transforms that rely on sufficient spatial sampling of the wavefield

## Slide 104: Ground roll suppression with adaptive subtraction
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
(Edme et al., 2014)

## Slide 105: Ground roll suppression with adaptive subtraction
Introduction / Polarization, CWT, SVD / Kettleman 6C survey / Polarization-based wave-mode separation
(Edme et al., 2014)
No spatial sampling requirements
Requires a model of the noise
Assumption that noise appears only on particular data components

## Slide 106
“FD Pressure” Idea
-Put the FD Stencil in the Earth-
(Courtesy of Fred Herkenhoff)

## Slide 107
Thanks for listening
1C
3C
6C
email: ohad@sep.stanford.edu
Notes: Seisballs are a derivation from Bob’s idea of using the BMW symbol