## Slide 1: Chapter 5 – EFWI of the Moere Vest data set

## Slide 2: Chapter 5
Regular spread:
141 4C nodes (Hydrophone + 3 Geophones)
250m between nodes
35km line
Long offset spread:
12 nodes (6 each side)
5km between nodes
adds 50km to line
2D 85 km receiver line
2D 110 km shot line (100 m sampling)
Offshore Norway - provided by Seabed Geosolutions

## Slide 3: The Moere Vest data
ROV camera during nodes deployment

## Slide 4: The Moere Vest data
ROV camera during nodes deployment

## Slide 5: The Moere Vest data

## Slide 6: The Moere Vest data
~ 55 km offset

## Slide 7: The Moere Vest data

## Slide 9
Multiples
Primary
reflections
Refractions
Refractions

## Slide 10: Inputs of Elastic FWI
Raw data
Data rotation
Receiver designature
De-bubble
Initial properties model
Initial Vp/Vs
Elastic RTM
Pre-processing of field data
Properties model

## Slide 11: Data pre-processing - Rotation
x
y
The initial orientation depends on the placement of the nodes by the ROV.
x’
y’
To find the right alignment, the data is rotated until the amplitude of the first break is maximum in the inline (x’) direction.
Raw data
Data rotation
Receiver de-signature
De-bubble

## Slide 12: Data pre-processing - Rotation

## Slide 13: Data pre-processing - Rotation

## Slide 14: Data pre-processing – Receiver designature
Raw data
Data rotation
Receiver de-signature
De-bubble
Data de-convolution (Wiener filter):
Notice the difference in receiver response of multi-component data.

## Slide 15: Data pre-processing – De-bubble
Raw data
Data rotation
Receiver de-signature
De-bubble

## Slide 16: Data pre-processing – De-bubble
Raw data
Data rotation
Receiver de-signature
De-bubble

## Slide 17: Data pre-processing – De-bubble
Raw data
Data rotation
Receiver de-signature
De-bubble

## Slide 18: Data pre-processing – De-bubble
Raw data
Data rotation
Receiver de-signature
De-bubble

## Slide 19: Data pre-processing – De-bubble
Raw data
Data rotation
Receiver de-signature
De-bubble

## Slide 20: Data pre-processing – De-bubble
Raw data
Data rotation
Receiver de-signature
De-bubble

## Slide 21: Initial properties model
Initial properties model
Initial Vp/Vs
Elastic RTM
Properties model
How to create an initial model for multi-parameter inversion?
  How smooth should be the initial model?
  What is the initial shear velocity?
  How do strong contrasts (basalt) affect elastic data?
INITIAL MODEL ESTIMATION FOR ELASTIC FWI IS CHALLENGING!

## Slide 25: LMO of field data
Moronfoye, et al., Upper-Crustal Structure of the Moere Vest Margin, offshore Norway, AGU, 2016
Initial properties model
Initial Vp/Vs
Elastic RTM
Horizontal geophone
Hydrophone

## Slide 26: LMO of field data
Moronfoye, et al., Upper-Crustal Structure of the Moere Vest Margin, offshore Norway, AGU, 2016
Vp/Vs ratio of 1.72 in the shallow sedimentary layer, for which Vs = 1340 m/s.
Initial properties model
Initial Vp/Vs
Elastic RTM

## Slide 27: Initial properties model
Initial properties model
Initial Vp/Vs
Elastic RTM
Vp = 2300 m/s
Vs = 1340 m/s
Vp = 1500 m/s
Vs = 0 m/s

## Slide 28: Building the initial model – Elastic RTM
Initial properties model
Initial Vp/Vs
Elastic RTM

## Slide 29: Building the initial model – Smooth initial model

## Slide 30: EFWI objective function

## Slide 31: EFWI objective function
Objective function
L2 norm
Elastic modeling operator
Property model (ρ,VP,VS)
Real or observed data
(4C: Hydrophone, vertical and horizontal geophones)

## Slide 32: EFWI objective function
Objective function
L2 norm
Property model (ρ,VP,VS)
Real or observed data
(4C: Hydrophone, vertical and horizontal geophones)
Python solver
Elastic modeling operator

## Slide 33: EFWI objective function
Objective function
L2 norm
Elastic modeling operator
Property model (ρ,VP,VS)
Real or observed data
(4C: Hydrophone, vertical and horizontal geophones)
Python solver
Elastic operator
*ALWAYS invert for the source wavelet

## Slide 34: EFWI objective function
Objective function
L2 norm
Elastic modeling operator
Property model (ρ,VP,VS)
Real or observed data
(4C: Hydrophone, vertical and horizontal geophones)
Python solver
Elastic operator
Pre-processing

## Slide 35: EFWI objective function
Objective function
L2 norm
Elastic modeling operator
Property model (ρ,VP,VS)
Real or observed data
(4C: Hydrophone, vertical and horizontal geophones)
Python solver
Elastic operator
Pre-processing
Initial model

## Slide 36: EFWI
I am using conjugate-gradients to calculate the search direction and the step lengths are found by parabolic search.
I start the inversion 2-5 Hz data, followed by 2-7.5 Hz and finally 2-10 Hz.
I tested 15 km offset, 12 s data and also 5 km offset, 5 s data.
I used spatial reciprocity to generate data in common receiver gathers and not common shot.

## Slide 37: EFWI with residual and gradient weights

## Slide 38: EFWI with residual and gradient weights

## Slide 39: EFWI with residual and gradient weights

## Slide 40: EFWI with residual and gradient weights

## Slide 41: EFWI with residual and gradient weights

## Slide 42: EFWI with residual and gradient weights

## Slide 43: EFWI with residual and gradient weights

## Slide 44: EFWI with residual and gradient weights

## Slide 45: EFWI with residual and gradient weights

## Slide 46: EFWI with residual and gradient weights - detail

## Slide 47: EFWI with residual and gradient weights

## Slide 48: EFWI with residual and gradient weights

## Slide 49: EFWI with residual and gradient weights

## Slide 50: EFWI with residual and gradient weights

## Slide 51: EFWI with residual and gradient weights

## Slide 52: EFWI with residual and gradient weights

## Slide 53: EFWI with residual and gradient weights

## Slide 54: EFWI with residual and gradient weights

## Slide 55: EFWI with residual and gradient weights

## Slide 56: EFWI with residual and gradient weights

## Slide 57: EFWI with residual and gradient weights

## Slide 58: EFWI with residual and gradient weights

## Slide 59: EFWI with residual and gradient weights

## Slide 60: EFWI with residual and gradient weights

## Slide 61: EFWI with residual and gradient weights

## Slide 62: Vp-Vs ratio of inverted models

## Slide 63: Vp-Vs ratio of inverted models
> 2.2 shales
~1.8 – 2.1 (basalt)
1.5 – 1.8 water saturated sandstones
Castagna, et al., 1985

## Slide 64: Comparing ERTM before and after EFWI

## Slide 65: Comparing ERTM before and after EFWI

## Slide 66: Comparing ERTM before and after EFWI

## Slide 67: Comparing ERTM before and after EFWI

## Slide 68: Comparing ERTM before and after EFWI

## Slide 69: Comparing ERTM before and after EFWI