## Slide 1: SEP seminar 9 March 2020
Side lobes and blocky inversion
Fault cores—if there will be time to spare

## Slide 2
Butterworth Vs Gaussian Wavelets
Blocky Wedge example

## Slide 3: Outline
I notice that students use Ricker or Butterworth wavelets in synthetics
I propose an alternative: Gaussian-Diff wavelet
  Minimal side lobes
I compare the two wavelets on a blocky wedge example to demonstrate an advantage of the Gaussian-Diff wavelet

## Slide 4: Gaussian wavelet: exp(-t/t)2 → exp(-ft)2
Sharp in the time domain
Small
t = 5 msec
Blunt in the time domain
Large
t = 125 msec
Scaled so that the areas are the same
Blunt in the frequency domain
Large 1/t
Sharp in the frequency domain
Small 1/t
Max (at zero) = 1
→
→

## Slide 5: Gaussian-Diff wavelet
→
Gaussian-Diff = Sharp Gaussian - Blunt Gaussian

## Slide 6: Butterworth and Ricker wavelets (on SU)
# GENERATE BFILT WAVELET
# Butterworth Wavelet from subfilt on a spike input
set BFILT = (subfilt verbose=1 fstoplo=1 fpasslo=5 fpasshi=60 fstophi=100)
suspike ntr=1 nspk=1 ix1=1 nt=1001 dt=0.002 it1=501 \
| sushw key=delrt a=-1000 | $BFILT …
subfilt: low-cut filter: npoles = 4, 3db point = 2.236304(Hz)
subfilt: high-cut filter: npoles = 10, 3db point = 78.350983(Hz)
#Generate Ricker Wavelet
suwaveform type=ricker1 dt=0.002 …

## Slide 7: Wavelets: Butterworth, Gauss-Diff, Ricker
→

## Slide 8: Blocky Wedge model: Acoustic Impedance

## Slide 9: Blocky Wedge: AI and Perfect Reflectivity

## Slide 10: Wavelets Gaussian vs Butterworth
→
This Butterworth has a very nice spectrum
But the side lobes are deeper and more numerous

## Slide 11: Data = Wavelet convolving Reflectivity

## Slide 12: AI from data (not blocky, not so good)

## Slide 13: Thresholding
A priori information (assumption)
The earth / the reservoir is blocky
Blocky acoustic impedance AI = r v
Spiky Reflectivity = (AIbelow - AIabove)/(AIbelow + AIabove)
The data are approximately the reflectivity
The data are not spiky because of the wavelet
Reflectivity = Spiky (Data)
  Sophisticated: entropy, kurtosis, …
  Simple (but essentially the same): Thresholding

## Slide 14: Thresholding and clipping
Thresholding
If(Input > Threshold) then Output = Input
else Output = 0
Clipping
If(Input < Clip) then Output = Input
else Output = Clip
Approximately:
Thresheld part
Input
Clipped part
Input
Thresheld part
Clipped part

## Slide 15: Threshold = Zero Clip = infinity (no-op)
If the Threshold is zero then everything is passed
(If the clip is zero then nothing is passed)
If the clip is infinity then everything is passed

## Slide 16: Threshold = Clip = 0.005
The threshold is too small to eliminate the sidelobes on the two wavelets

## Slide 17: Threshold = Clip = 0.01
The threshold is too small to eliminate the sidelobes on the Butterworth wavelet
But it is large enough to eliminate the side lobes on the Gaussian wavelet

## Slide 18: Threshold = Clip = 0.02
The threshold is still too small to eliminate the sidelobes on the Butterworth wavelet
But it is of course large enough to eliminate the side lobes on the Gaussian wavelet

## Slide 19: Threshold = Clip = 0.03
The threshold is still too small to eliminate the sidelobes on the Butterworth wavelet
But it is of course large enough to eliminate the side lobes on the Gaussian wavelet

## Slide 20: Threshold = Clip = 0.04
The threshold is still too small to eliminate the sidelobes on the Butterworth wavelet
But it is of course large enough to eliminate the side lobes on the Gaussian wavelet

## Slide 21: Threshold = Clip = 0.05
The threshold is still too small to eliminate the sidelobes on the Butterworth wavelet
But it is of course large enough to eliminate the side lobes on the Gaussian wavelet

## Slide 22: Threshold = Clip = 0.06
The threshold is large enough to eliminate the sidelobes on the Butterworth wavelet
But it is of course large enough to eliminate the side lobes on the Gaussian wavelet

## Slide 23: Thresheld data

## Slide 24: Unthreshed Data

## Slide 25: Thresheld data

## Slide 26: AI from thresheld data (blocky)

## Slide 27: AI from thresheld data (blocky)

## Slide 28: Summary
The Gaussian-Diff wavelets has less side-lobes
It does not matter much …
Until I try to impose blockiness by sparsity of reflectivity, using thresholding
The wavelet with less side lobes is easier to threshold

## Slide 29: Post summary: try a softer butterworth?
Hard: low-cut: npoles = 4, high-cut: npoles = 10
Soft: low-cut: npoles = 4, high-cut: npoles = 2

## Slide 30: Post Summary
Butterworth is minimum phase (although in subfilt the default is ‘zerophase=1’. You have to put zerophase=0 to get minimum phase)
If you want zero phase, which you do for inversion for acoustic impedance, then use gauss-diff
If you want minimum phase, then maybe butterworth, maybe leaky integration. Probably not Gauss-Diff taken via Kolmogoroff to make it minimum phase

## Slide 31: Minimum phase Butterworth

## Slide 32: Soft Thresholding and Clipping?
Hard thresholding and hard clipping are not reversible
Soft clipping is
Soft thresholding?

## Slide 33
Fault-cores
and
Fault plane reflections

## Slide 34: Do you see a problem here?

## Slide 35: Fault core
Faults are not “clean cuts”
There are broken zones
I thanks Professor David Pollard for teaching me about them and for the picture

## Slide 36: Small faults: thin cores
In large scale the fault core is thick enough to reflect seismic waves

## Slide 37
A. Torabi et al. Geological Society, London, Special Publications 2019;496:SP496-2018-151

## Slide 38: From Dave Hale’s thesis
Fault plane reflections (?)
Negative polarity (?)
Softer (?)
Fault plane reflections and layer edges may not image at the same place because of
  2D data
  Isotropic processing

## Slide 39: From Dave Hale’s thesis

## Slide 40: From Dave Hale’s thesis

## Slide 41: From Dave Hale’s thesis

## Slide 42: From Dave Hale’s thesis

## Slide 43: From Dave Hale’s thesis

## Slide 44: From Dave Hale’s thesis

## Slide 45: Summary
Faults have cores
  A zone that was changed and is different from the formations on either side of the fault
  Small faults have thin or no cores
  Large faults have cores that are thick enough to reflect seismic waves
Programs that generate reflectivity from geological scenarios need to take fault cores into account