## Slide 1: Broadband Processing and Imaging: Retaining low frequencies in migration

## Slide 2: Low frequency signal is a challenge
Sources that produce low frequency waves are larger and require more energy than high frequency sources
Receivers have evolved to record what sources produce
  Receivers are not the limiting factor. However, low frequency receiver challenges: instrument noise, omni-tilt
Source and receiver ghosts reduce low frequency signal
Ambient ocean noise is “red” (low frequency)
Retaining low frequency signal in broadband processing and imaging is a challenge

## Slide 3: Low frequency challenges and solutions
Low frequency sources
Multi-component receivers
Ambient Ocean noise

## Slide 4: Broadband processing and imaging
Low-frequency sources (big and expensive)
  And their designature
Low-frequency receivers (expensive)
  And their designature: 6-12 dB/octave and 90o-180ophase
Deghosting is more important and can be tricky
  Surface reflection coefficient is stronger at lower frequency
  Multi-component helps
Imaging: must not lose or damage the low frequency signal when we migrate

## Slide 5: Spoiler Alert
Input Flat Event | Fourier Migration | 2D Kirchhoff Migration |  |  | 
 |  |  |  | No Half-diff | Half-Diff
Kirchhoff migration programs have problems in imaging low frequency signal without artifacts
Why it is important
How these problems can be solved
Explore the low frequency limits of migration
Signal down to 0 Hz
No Problems
Yes Problem
Problem solved

## Slide 6: Post spoiler alert
We could stop here
  45 minute lecture into a telegram: diff aka rho filter: http://sepwww.stanford.edu/sep/prof/iei/slnt/paper_html/node18.html
Anybody in a hurry can leave now
But if you stay, you will learn about imaging, geometry, Z transforms, and (if you are like me) have fun with numerical experiments

## Slide 7: History of Migration
Kirchhoff methods (late 1960s... CSM, 1978-80s)
  NMO-Stacking had been in use as summation over hyperbolas in the offset direction
  In the mid-point direction it became Kirchhoff Migration
Finite Differencing methods: Claerbout (early 1970s)
Fourier Transform methods: Gazdag, Stolt (late 1970s)
Reverse Time Migration (early 1980s)
Least Squares Migration (Theory: late 1980s)
Joint primary and multiple imaging (2000s)
In practice High Performance Parallel Computing

## Slide 8: Do we care about Kirchhoff?
For some time (2D) we did not care because Finite-Differencing and Fourier methods do not have this problem
However, when we started doing 3D, Kirchhoff methods came back in great force
Even now, with WEM, Reverse Time, FWI, and LSMig, Kirchhoff is important, because
  “Fast track” processing (next iteration after “brute-stack”)
  Iterative velocity model building
  LSMig can be done well with Kirchhoff (not exclusive)
  Irregular acquisition geometry

## Slide 9: 2D: approximately regular surveys
Data(Sht,Rcv,Time)
Land
Marine (streamers)
OBC (cables)
OBN (nodes)
Ocean Bottom (also Marine)
Image(x,z)
3D
Migration
&
Stacking
2D

## Slide 10: 3D seismic surveys are 5D seismic data
3D Image(x,y,z)
5D Data(Shot, Receiver, Time)
  Shot(x,y) and Receiver(x,y)
  Surface data are 5D
  For VSP and Cross well, the data are 7D with Shot(x,y,z) and Receiver(x,y,z)
Data(Sht,Rcv,Time)
Image(x,y,z)
5D
Migration
&
Stacking
3D

## Slide 11: Surface+borehole surveys with are 7D
3D Image(x,y,z)
5D Data(Shot, Receiver, Time)
  Shot(x,y) and Receiver(x,y)
  Surface data are 5D
  For VSP and Cross well, the data are 7D with Shot(x,y,z) and Receiver(x,y,z)
Data(Sht,Rcv,Time)
Image(x,y,z)
7D
Migration
&
Stacking
3D

## Slide 12: Ideal 3D surveys: shots and receivers everywhere
3D seismic survey is 5D data
3D Image(x,y,z)
5D Data(Shot, Receiver, Time)
  Shot(x,y) and Receiver(x,y)
  For VSP and Cross well, the data are 7D with Shot(x,y,z) and Receiver(x,y,z)
We can’t have fully sampled 5D, let alone 7D, data
  At best 3D subsets

## Slide 13: Towed Streamers
Robertson et al, 2016. GeoExPro
Fontana, Polarcus
The 5D data are a collection of 3D gathers
Very well sampled in Time
Very well sampled in the Receiverx direction
Well sampled in the Shotx direction
Poorly sampled in the Receivery direction
Very Poorly sampled in the Shoty direction
And there is feathering which is a nuisance but it helps with the poor cross-line Y coverage

## Slide 14: Wide Azimuth Towed Streamers
Robertson et al, 2016. GeoExPro
Narrow Azimuth (NATS)
Multi Azimuth (MAZ)
Wide Azimuth (WATS)
Full Azimuth (FAZ) …
  … but coil is very irregular
These help with wide azimuth for better sub-surface coverage under salt, but do not provide regular geometry
Coil (Western Geco)

## Slide 15: Land surveys are irregular (“brick” shown here)
G. Vermeer, 2004. CSEG Recorder

## Slide 16: Land surveys are irregular
Dombrowski et al, 2017. EBN Utrecht

## Slide 17: Cross-spread geometry (Time, Rcvx ,Shty)
Vermeer, 1998. Geophysics
Tim Dean, 2012. Preview
The 5D data are a collection of 3D gathers
Very well sampled in Time
Very well sampled in the Receiverx direction
Well sampled in the Shoty direction
Poorly sampled in the Receivery direction
Very Poorly sampled in the Shotx direction
There are
Irregularities on Land
Less irregularities with OBC
However, keep in mind that Cross-Spread Data(Receiverx,Shoty ,Time) is not a wavefield from a physical experiment

## Slide 18: Ocean Bottom Nodes (Time, Shotx ,Shoty)
Dense shot carpet
Sparse nodes
Common Receiver Gather (3D subset)
  Well sampled in Time
  Well sampled in Shotx
  Well sampled in Shoty
  Poorly sampled in Receiverx
  Poorly sampled in Receivery
  Slightly randomized shot X and Y
  Obstructions: holes in the shot carpet
  Using reciprocity the CRGs are a wavefield from a physical experiment!
Hardouin et al, EAGE 2011

## Slide 19: Compressive sensing
Intentional random geometry
Less sampling (spatial aliasing) artifacts
To understand why we need to go through LSM (=Least Square Migration, but it could be L1M, etc.)
And keep in mind that matrices with random numbers are “well conditioned”. They are often invertible. Moreover, their transpose is often a good approximation to their inverse.

## Slide 20: Do we care about Kirchhoff? YES
Irregular geometry motivating Kirchhoff
Streamer data: feathering
Land data: irregular (brick worse than cross-spread)
OBC: regular cross spread data but not a wavefield
OBN: holes in the shot carpet due to obstructions and slight irregularities in shot post-plot positions
Compressive sensing: intentional irregularities

## Slide 21: Simple overburden: Kirchhoff vs RTM
Up Kirchhoff
Down Kirchhoff
Up LSRTM
Down LSRTM
Joint LSRTM
Cascadia data example thanks to University of Victoria

## Slide 22: VSP imaging is almost always Kirchhoff
https://csegrecorder.com/articles/view/vsp-for-the-interpreter-processor-for-2001-and-beyond-part-1
https://www.sercel.com/products/Lists/ProductPublication/Reducing%20Drilling%20Risk%20on%20Culzean%20using%20WAVI-VSP_Oct2019.pdf
Far offset
Near offset

## Slide 23: Impulse response of simple Kirchhoff

## Slide 24: Flat event response of simple Kirchhoff
Sum across to calculate the flat event response
This is good
This precursor is not good

## Slide 25: Retaining low frequency in migration
Kirchhoff methods produced a low frequency precursor
  It can be attenuated by low-cut filtering. BUT …
  Broadband processing: stay away from low-cut filters!
Questions:
  Is this an inherent problem for all migration methods?
  Do we care (about Kirchhoff)?
  What is the best solution?

## Slide 26: 1. Gazdag method: DC okay in theory
No problem at w=0
  Downward continuation step
  When w is zero, so are kx and kz
  (When w=0, kz is imaginary if kx is not zero and real)

## Slide 27: 1. Gazdag method: in practice
Let’s migrate some synthetic data with DC
We looked at migration impulse responses
Used the Gazdag method implemented on SU
  http://sepwww.stanford.edu/oldsep/cliner/files/suhelp/sugazmig.txt
Following slides
  I show the impulses and their responses
  And I summed across to get flat event responses

## Slide 28: Bandlimited wavelet: High-cut but no low-cut
Chose to generate a Gaussian wavelet
  No low-cut, only hi-cut
Sampling interval Dt = 1 millisecond
Gaussian width = 4 milliseconds
  High cut approximately at 125 Hz

## Slide 29: Gaussian wavelet
Time domain
Frequency domain spectrum
Time domain
No low frequency limit!

## Slide 30: Migration impulse response
T-X
F-X
F-K

## Slide 31: Migration impulse response
Migration impulse response is not zero phase!

## Slide 32: Impulse response → flat event response
Perfect zero-phase
Flat event response
Sum across to calculate the flat event response
zero

## Slide 33: Summary so far
Gazdag’s phase shift does not have any problem with low frequency signal
  Down to zero frequency!
Simple Kirchhoff does have a problem
  Low-frequency precursor problem
  Well known since early 70s
  Motivated FD & FT migration
Gazdag
Kirchhoff

## Slide 34: Fixing Kirchhoff (in 3D it’s more practical)
Norm Bleistein (1987 and before): “You need a derivative (in 3D Kichhoff) or a half-derivative (in 2D Kirchhoff)”
We could calculate the Green function of Gazdag (stationary phase)
Alternative method for the analysis
  Numerically calculate a flat even response of simple Kirchhoff, without any low-cut, and then with half/full diff
  We’ll do it for 3 frequencies
  Limit the migration aperture
  2D and 3D

## Slide 35: Flat event response
To calculate a flat event response of a Kirchhoff migration
  Sum migration impulse response over x, just like we did for Gazdag
  But this time: frequency domain Kirchhoff. That is (w,x) domain
  1996 paper https://doi.org/10.1190/1.1887374 (which was for Kirchhoff DMO)

## Slide 36: Kirchhoff PULL
Foreach image point (x,z)
Output(x,z) = SUMl Input[l,t(x-l,z)]
(x,z) is the image point
SUMl is summation over l
t() is the hyperbola
(vt()/2)2 = z2 + (x-l)2
(x,z)
(l,z=0)

## Slide 37: Results—4km aperture, t0=1 seconds
Observations
Low frequency: no convergence
Half integral
  Low frequencies scaled up
  “High” frequencies converge to points almost exactly on the sqrt(i) line  45 degree phase
  There is a factor 2 scale in amplitude for every factor 4 in frequency  1/sqrt(w)
  Hence: 1/sqrt(iw)  half integral!
  we need a Half derivative to prevent the half integral
5 Hz
20 Hz
80 Hz

## Slide 38: Results—4km aperture, t0=4 seconds
Observations
Almost exactly as t0=1
There is a dependency on frequency but less so on t0−convergence depends on wt0 >>1)
5 Hz
20 Hz
80 Hz

## Slide 39: Results with half derivative option on, t0=1
5 Hz
20 Hz
80 Hz
Observations
20Hz and 80Hz converge to about the same point very near the real axis
Slightly off
Why? high frequency approximation, sure, but maybe there is more to it, because it is much worse below 5Hz
Low frequencies need long aperture and time to converge

## Slide 40: Results with half derivative option on, t0=4
Observations
20Hz and 80Hz converge to about the same point very near the real axis)
Less error than t0=1 because wt0 is four times larger, so high frequency approximation is better
Low frequencies need long aperture and time to converge
5 Hz
20 Hz
80 Hz

## Slide 41: Summary of what we learned from the spirals
Putting a half derivative term in a Kirchhoff migration is needed (Norm Bleistein was right)
Without a half derivative term, the results have a half-integral error
  Which can be corrected by half derivative post migration
In 3D it would be a full derivative because 3D can be done by two orthogonal passes of 2D
  The post 3D Kirchhoff migration correction would be a full derivative
Not sure about the following minor issues
  The Jacobian: dropping it does not make a substantial difference except that without it convergence is a bit faster (minor effect, bumped to “spare-slides”)
  Converging to (950, almost 0) instead of converging to (1,0) because I didn’t normalize by the number of traces in the aperture

## Slide 42: Now let’s apply half derivative to test it
Half derivative is simple in the frequency domain, sqrt(iw), but tricky in the time domain
  An example of half is more expensive than one
Implemented a finite differencing half-diff based on Taylor series of sqrt(1-Z)
  1-Z is of course Finite Differencing full derivative
  Can be either causal or anti-causal
Found that we need an anti-causal half derivative.
  Causal half-derivative made things worse

## Slide 43: Taylor series: sqrt(1-Z) = sqrt(1+x) (x=-Z)
https://planetmath.org/TaylorExpansionOfsqrt1x
Causal
Minimum-phase
Anti-Causal
Maximum-phase

## Slide 44: Testing the half-derivative program
Applying causal half derivative twice gives a causal full derivative
Applying anti-causal half derivative twice gives an anti-causal full derivative
Causal
Minimum-phase
Anti-Causal
Maximum-phase
Time
Time

## Slide 45: Testing the half-derivative program
Time
Time
Time
Time
Applying causal half derivative twice gives a causal full derivative
Applying anti-causal half derivative twice gives an anti-causal full derivative
Impulse response of an anti-causal half derivative after a causal half derivative
Impulse response of a causal half derivative after an anti-causal half derivative

## Slide 46: No Half Diff—Not good
Poor-man’s Kirchhoff Impulse Response using NMO
No Half Diff
Summing across to get a Flat Event Response

## Slide 47: Causal Half Diff—even worse!
Poor-man’s Kirchhoff Impulse Response using NMO
Causal Half Diff
Summing across to get a Flat Event Response

## Slide 48: Anti-causal Half Diff—pretty good
Poor-man’s Kirchhoff Impulse Response using NMO
Anti-Causal Half Diff
Summing across to get a Flat Event Response

## Slide 49: Comparing the three outputs
The red, which is no half diff has what looks like an anti-causal half integral
The green which is the causal Half Diff is the worst: approximately 45o+45o !
The blue, which is the anti-causal half diff is good
  Not exactly… probably poor approximation of finite differencing half derivative

## Slide 50: 3D
In 3D, Kirchhoff theory predicts a need for a full time derivative
We will test it with a 3D poor-man’s-Kirchhoff-using—NMO-of-a-flat plane
We will stack across the semispherical impulse response to get the flat event response
  With and without full derivative

## Slide 51: 3D Flat event response (sunmo default sscale=1)
Just sum across IR
Sum IR after diff
Sum IR after diff
and flip sign
Sum IR before diff
and flip sign

## Slide 52: Flat event responses (sscale=0 in sunmo)
Just sum across IR
Sum IR after diff
Sum IR after diff
and flip sign
Sum IR before diff
and flip sign
Perfect!

## Slide 53: Summary so far—significant problem ~solved
Input Flat Event | Gazdag Migration | Kirchhoff Migration |  |  | 
 |  | sscale on |  | sscale off | 
 |  | Raw | Half Diff | Raw | Half Diff
Perfect!
Good!
Good!

## Slide 54: Low frequency imaging
Velocity model building such as FWI benefits from low frequency signal
  Avoiding local minima (“cycle skips”) in fitting the data
Imaging low frequencies should also benefit
  Sub-salt/Sub-basalt/Blocky reservoir model building
But it seems like imaging has a low frequency limit!
  In Kirchhoff there is a stationary phase approximation and a zero divided by zero implied by correcting/pre-empting a half integral by a half derivative: sqrt(iw) / (1/sqrt(iw)
  FK and FD migration methods will also have a problem with very low frequencies for any shallow reflector that is not flat

## Slide 55: Spiral plots for Ultra Low Frequency (<<5Hz)
With maximum migration aperture of 4km they do not converge at 0.5 Hz
With up to 4 km aperture, we will not be able to image 1Hz even if we had 1Hz sources and receivers
4 km aperture
0.5 Hz
1 Hz
2 Hz

## Slide 56: Spiral plots for Ultra Low Frequency (<<5Hz)
With 40 km aperture they converge better
We can image 1 Hz signal if had
  Ultra low frequency sources and receivers
  Ultra long offset
  And are willing to tolerate or fix incomplete convergence
40 km aperture
0.5 Hz
1 Hz
2 Hz

## Slide 57: Summary
3D Kirchhoff migration requires a time differentiator
  A differentiator is very simple: D(Z) = 1 – Z
  The only slight complication is that it should be anti-causal (if not, the sign is reversed)
  It’s better applied prestack
2D is much more difficult: we need a half differentiator
  A half differentiator is difficult in the time domain (and what would be the causality in the frequency domain?
  It must be anti-causal (if not, it’s a mess)
The spirals show that the ultra low frequencies (1Hz) won’t converge with a reasonable aperture. However, the time domain testing shows that whatever errors are very small