## Slide 1: Wavefield continuation theory, Born approximation, imaging principles Migration methods: WEM, RTM, Kirchhoff High-resolution acquisition, including: broadband sources and receivers, dense time and space sampling, source and receiver designature, deghosting, and examples of how shear waves may and may not improve resolution Practical problems in imaging, including: angle control, anisotropy, land, and many more Velocity estimation, shallow and deep OBN hardware, acquisition geometries, operations, and processing Towards high-resolution imaging: least-squares migration, imaging multiples, broadband imaging Towards unconventional high-resolution imaging: magical thinking? (Sparsity, diffraction imaging, superresolution)

## Slide 2: Seismic imaging Principles and practice
Sam Gray – modified and expanded from CGG training
Includes RTM synthetic example from James Sun

## Slide 3: Wavefield Extrapolation

## Slide 4: Superposition principle
depth
When energy hits a diffracting point it re-emits energy in all directions. The diffracting point is like a point source for a new wavefront.

## Slide 5: Superposition principle
depth
When energy hits a diffracting point it re-emits energy in all directions. The diffracting point is like a point source for a new wavefront.

## Slide 6: Superposition principle
depth
When energy hits a diffracting point it re-emits energy in all directions. The diffracting point is like a point source for a new wavefront.

## Slide 7: Superposition principle
depth
When energy hits a diffracting point it re-emits energy in all directions. The diffracting point is like a point source for a new wavefront.

## Slide 8: Superposition principle
depth
When energy hits a diffracting point it re-emits energy in all directions. The diffracting point is like a point source for a new wavefront.
A similar experiment: a seismic source emits energy in all directions.

## Slide 9: Superposition principle
depth
When energy hits a diffracting point it re-emits energy in all directions. The diffracting point is like a point source for a new wavefront.
A similar experiment: a seismic source emits energy in all directions.

## Slide 10: Superposition principle
depth
When energy hits a diffracting point it re-emits energy in all directions. The diffracting point is like a point source for a new wavefront.
A similar experiment: a seismic source emits energy in all directions.

## Slide 11: Superposition principle
We can add more and more diffractors or point sources emitting energy at the same time and show the wavefronts spreading out with time. Linear superposition of wavefields from multiple sources.
depth

## Slide 12: Superposition principle
The wavefronts emitted from these diffractors or point sources will superimpose on each other, constructively interfering in some places and destructively interfering in others.
depth

## Slide 13: Superposition principle
As we add more and more diffractors or point sources we start to approximate a continuous reflection event, or wavefront.
depth

## Slide 14: Superposition principle
As we add more and more diffractors or point sources we start to approximate a continuous reflection event, or wavefront.
depth

## Slide 15: Superposition principle
As we add more and more diffractors or point sources we start to approximate a continuous reflection event.
What’s missing in this picture?
depth

## Slide 16: Superposition principle
As we add more and more diffractors or point sources we start to approximate a continuous reflection event.
What’s missing in this picture?
depth

## Slide 17: Superposition principle holds for sources, not diffractors
As we add more and more diffractors or point sources we start to approximate a continuous reflection event.
What’s missing in this picture? Assumes all diffractors are independent of each other. In reality, diffractors interact: Multiple diffractions.
depth
But we will usually pretend that superposition holds for diffractors too.

## Slide 18: Superposition principle holds for sources, not diffractors
The individual diffracted wavefronts superimpose to form the wavefront that we would get from a continuous reflector.
depth
But we will usually pretend that superposition holds for diffractors too.

## Slide 19: Superposition principle holds for sources, not diffractors
“Common tangents”: constructive and destructive interference.
depth
But we will usually pretend that superposition holds for diffractors too.

## Slide 20: Superposition principle
The resulting wavefield has plane wavefronts created from the continuous part of the event and the diffracted wavefronts from the discontinuous edges.
depth

## Slide 21: Huygens’ principle
Huygens’ principle states that each point on the wavefront at a specific time can be regarded as the source of a subsequent wave. Destructive interference destroys the subsequent waves except along the common tangent producing a new wavefront.
Christiaan Huygens
1629-1695
depth

## Slide 22: Huygens’ principle
We can plot the wavefront at time T + dT from each new point source along the original wavefront.
depth

## Slide 23: Huygens’ principle
That is, the wavefront at time T + dT is built from each new point source along the original wavefront.
depth

## Slide 24: Huygens’ principle
Huygens waves propagate forward in time, and outward from the source.
Keep this part.
Discard this part.
depth

## Slide 25: Huygens’ principle
Huygens waves propagate forward in time, and outward from the source.
depth

## Slide 26: Huygens’ principle
Huygens waves propagate forward in time, and outward from the source.
depth

## Slide 27: Huygens’ principle
Huygens waves propagate forward in time, and outward from the source.
depth

## Slide 28: Huygens’ principle
Huygens waves propagate forward in time, and outward from the source.
depth

## Slide 29: Huygens’ principle
Huygens waves propagate forward in time, and outward from the source.
But they could propagate backward in time, or inward to the source.
depth

## Slide 30: Huygens’ principle
Repeating for all the new point sources we can see the wavefront built up at time T + dT or indeed T - dT. Therefore if we know the wavefield at a snapshot time T and we know the velocity field, then we can predict the wavefield at time T + dT or indeed T - dT. This is the basis behind forward and reverse wavefield extrapolation techniques.
depth

## Slide 31: Huygens’ principle is incomplete
As stated, Huygens’ principle allows waves to travel forward in space/time, but not backward in space/time.
Huygens’ principle is stated for waves traveling without obstruction, i.e., no barriers.
Wave refraction in the manner of Huygens.
From Wikipedia,
“Huygens – Fresnel Principle”.

## Slide 32: Huygens’ principle is incomplete
As stated, Huygens’ principle allows waves to travel forward in space/time, but not backward in space/time.
Huygens’ principle is stated for waves traveling without obstruction, i.e., no barriers.
Wave refraction in the manner of Huygens.
From Wikipedia,
“Huygens – Fresnel Principle”.

## Slide 33: Huygens’ principle is incomplete
As stated, Huygens’ principle allows waves to travel forward in space/time, but not backward in space/time.
Huygens’ principle is stated for waves traveling without obstruction, i.e., no barriers.
Wave refraction in the manner of Huygens.
From Wikipedia,
“Huygens – Fresnel Principle”.

## Slide 34: Huygens’ principle is incomplete
As noted, Huygens’ principle provides for waves traveling forward in space/time, but not backward in space/time.
Huygens’ principle is stated for waves traveling without obstruction, i.e., no barriers.
Wave diffraction in the manner of Huygens and Fresnel.
From Wikipedia,
“Huygens – Fresnel Principle”.

## Slide 35: Huygens’ principle applied to migration
As stated, Huygens’ principle allows waves to travel forward in space, but not backward in space.
Most migration methods use Huygens’ principle, both forward and backward in time.
Does RTM use Huygens’ principle?

## Slide 36: Theory of standard migration*
Standard migration is a combination of
Superposition
Huygens’ principle, forward and backward in time
Imaging condition (coming soon)
*What is “standard migration”?

## Slide 37: What is “standard migration”?
Standard migration
Single scatter

## Slide 38: What is “standard migration”?
Multiple scatter
Refraction
NOT standard migration
Liu et al., 2011

## Slide 39: Off on a tangent: Are these “single scatter?”
Weglein et al. (1997)

## Slide 40: Off on a tangent: Are these “single scatter?”
Weglein et al. (1997)

## Slide 41: Theory of standard migration
Standard migration is a combination of
Superposition of wave propagation (correct)
Huygens’ principle, forward and backward in time
Single scatter (superposition of diffraction: Born approximation)
Imaging condition (coming soon)
Max Born
1882-1970

## Slide 42: Theory of standard migration
Born approximation:
  Total wavefield = reference wavefield + scattered wavefield,
  where velocity has been split into
  reference velocity + velocity perturbation.
  Scattered wavefield is a volume integral of velocity perturbation:
  )
  ) is the propagator from to
xr
x
z
e.g.,

## Slide 43: Theory of standard migration
Born approximation:
  Total wavefield = reference wavefield + scattered wavefield,
  where velocity has been split into
  reference velocity + velocity perturbation.
  Scattered wavefield is a volume integral of velocity perturbation:
  )
  ) is the propagator from to
xr
x
z
e.g.,

## Slide 44: Theory of standard migration
Born approximation:
  Total wavefield = reference wavefield + scattered wavefield,
  where velocity has been split into
  reference velocity + velocity perturbation.
  Scattered wavefield is a volume integral of velocity perturbation:
  )
  ) is the propagator from to
xr
x2
z
x1
Not allowed!
e.g.,

## Slide 45: Theory of standard migration
Born approximation:
  Total wavefield = reference wavefield + scattered wavefield,
  where velocity has been split into
  reference velocity + velocity perturbation.
  Scattered wavefield is a volume integral of velocity perturbation:
  )
Recorded data
Unknown (“image”)
Unknown “propagators”

## Slide 46: Theory of standard migration
Born approximation:
  Total wavefield = reference wavefield + scattered wavefield,
  where velocity has been split into
  reference velocity + velocity perturbation.
  Scattered wavefield is a volume integral of velocity perturbation:
  )
Recorded data
Unknown (“image”)
Known “reference propagators”

## Slide 47: Theory of standard migration
Born approximation:
  )
Recorded data
Unknown (“image”)
Known “reference propagators”
One equation, one unknown. “Simply” invert for

## Slide 48: Theory of standard migration
Born approximation:
  )
One equation, one unknown. “Simply” invert for
Hint:

## Slide 49: Theory of standard migration
Born approximation:
  )
One equation, one unknown. “Simply” invert for
Hint:
What are the mathematical units?

## Slide 50: Total wavefield = reference wavefield + scattered wavefield

## Slide 51: Total wavefield = reference wavefield + scattered wavefield
Bad choice of reference velocity:
Too slow!

## Slide 52: Total wavefield = reference wavefield + scattered wavefield
Scattered wavefield =
(Total wavefield – reference wavefield) is large. Born approximation is bad for this reference velocity.

## Slide 53: Total wavefield = reference wavefield + scattered wavefield

## Slide 54: Total wavefield = reference wavefield + scattered wavefield
Bad choice of reference velocity:
Too slow!

## Slide 55: Total wavefield = reference wavefield + scattered wavefield
Better choice of reference velocity

## Slide 56: Theory of standard migration
Standard migration is a combination of
Superposition of wave propagation (correct)
Huygens principle, forward and backward in time
Imaging condition (coming soon)
Single scatter (Born approximation) :
  Superposition of response (approximate) :
  Adding one more scatterer / diffractor adds one more diffraction response to the recorded wavefield : Single scatter happens when either :
    Applying WKBJ to the source and receiver propagators ; or
    Smoothing the velocity field.
    Both rely on high-frequency asymptotics (next).
)
WKBJ: “J” = Sir Harold Jeffreys 1891-1989

## Slide 57: Theory of standard migration
Velocity smoothing and high-frequency asymptotics:
No smoothing : waves of all frequencies WILL reflect. BAD.
Long-wavelength smoothing : waves of all frequencies WILL NOT reflect. GOOD.
Short-wavelength smoothing :
low-frequency waves WILL reflect. BAD.

## Slide 58: Theory of standard migration
Velocity smoothing and high-frequency asymptotics:
No smoothing : waves of all frequencies WILL reflect. BAD.
Short-wavelength smoothing :
high-frequency waves WILL NOT reflect. GOOD.
Long-wavelength smoothing : waves of all frequencies WILL NOT reflect. GOOD.

## Slide 59: Theory of standard migration
Velocity smoothing and high-frequency asymptotics:
No smoothing : waves of all frequencies WILL reflect. BAD.
Short-wavelength smoothing :
high-frequency waves WILL NOT reflect. GOOD.
Long-wavelength smoothing : waves of all frequencies WILL NOT reflect. GOOD.
“Good”, but not always accurate!

## Slide 60: Theory of standard migration
Velocity smoothing and high-frequency asymptotics:
RTM crosstalk from not enough smoothing
OWEM : asymptotics honored automatically

## Slide 61: Theory of standard migration
Velocity smoothing and high-frequency asymptotics:
No smoothing : waves of all frequencies WILL reflect. BAD.
Short-wavelength smoothing :
high-frequency waves WILL NOT reflect. GOOD.
Long-wavelength smoothing : waves of all frequencies WILL NOT reflect. GOOD.
What frequencies are“high”?

## Slide 62: The source wavefield, plus unwanted receiver wavefield
Acknowledgement to SINTEF, Rita Streich
And if we know the wavefield and its time derivative at a specific time t we can also extrapolate the wavefield in reverse.
We can use wavefield extrapolation to forward propagate a source wavelet through a velocity model and record the resultant wavefield at the surface to form a gather.

## Slide 63: The receiver wavefield, plus unwanted source wavefield
Acknowledgement to SINTEF, Rita Streich
And if we know the wavefield and its time derivative at a specific time t we can also extrapolate the wavefield in reverse.
We can use wavefield extrapolation to forward propagate a source wavelet through a velocity model and record the resultant wavefield at the surface to form a gather.

## Slide 64: The imaging condition uses source and receiver wavefields
And if we know the wavefield and its time derivative at a specific time t we can also extrapolate the wavefield in reverse.
We can use wavefield extrapolation to forward propagate a source wavelet through a velocity model and record the resultant wavefield at the surface to form a gather.
Is that the same as migration?

## Slide 65: Wave equation migration (Claerbout, 1970-1971)
The imaging principle:
“Reflectors exist in the earth at places where the onset of the downgoing wave is time coincident with an upgoing wave.” – Claerbout (1971)

## Slide 66: Wave equation migration (Claerbout, 1970-1971)
The imaging principle:
“Reflectors exist in the earth at places where the onset of the downgoing wave is time coincident with an upgoing wave.” – Claerbout (1971)
D

## Slide 67: Wave equation migration (Claerbout, 1970-1971)
The imaging principle:
“Reflectors exist in the earth at places where the onset of the downgoing wave is time coincident with an upgoing wave.” – Claerbout (1971)
D

## Slide 68: Wave equation migration (Claerbout, 1970-1971)
The imaging principle:
“Reflectors exist in the earth at places where the onset of the downgoing wave is time coincident with an upgoing wave.” – Claerbout (1971)
U = R D
R = U / D
D
U

## Slide 69: Wave equation migration (Claerbout, 1970-1971)
The imaging principle:
“Reflectors exist in the earth at places where the onset of the downgoing wave is time coincident with an upgoing wave.” – Claerbout (1971)

## Slide 70: Wave equation migration (Claerbout, 1970-1971)
The imaging principle:
“Reflectors exist in the earth at places where the onset of the downgoing wave is time coincident with an upgoing wave.” – Claerbout (1971)
How are these two related?

## Slide 71: Wave equation migration (Claerbout, 1970-1971)
The imaging principle:
“Reflectors exist in the earth at places where the onset of the downgoing wave is time coincident with an upgoing wave.” – Claerbout (1971)
R = ∫ U / D dω
R = ∫ U D* dω

## Slide 72: Wave equation migration (Claerbout, 1970-1971)
The imaging principle:
“Reflectors exist in the earth at places where the onset of the downgoing wave is time coincident with an upgoing wave.” – Claerbout (1971)
R = ∫ U / D dω
R = ∫ U D* dω
What are the mathematical units?

## Slide 73: Wave equation migration (Claerbout, 1970-1971)
The imaging principle:
“Reflectors exist in the earth at places where the onset of the downgoing wave is time coincident with an upgoing wave.” – Claerbout (1971)
R = ∫ U / D dω
R = ∫ U D* dω
What are the mathematical units?
What are the best mathematical units for a migrated image?

## Slide 74: Wave equation migration (Claerbout, 1970-1971)
The acoustic wave equation
Very slow to compute in 1970
Two-way (no “downgoing” and “upgoing”)
A new (“parabolic”, low-dip) wave equation (Claerbout and Johnson, 1971)
Much faster to compute
One-way
The imaging principle:
“Reflectors exist in the earth at places where the onset of the downgoing wave is time coincident with an upgoing wave.” – Claerbout (1971)

## Slide 75: Parabolic wave equation
M. Leontovich and V. Fock, Solution of the problem of propagation of electromagnetic waves along the earth’s surface by the method of parabolic equation, Acad. Sci.
USSR. J. Phys. 10 (1946), 13–24.
USSR: Laser optics, late 1960’s
Geophysics: Claerbout, c. 1969
Necessity is the mother of invention
Underwater acoustics, early 1970’s

## Slide 76: The invention of wave-equation migration
Claerbout, 1971

## Slide 77: The invention of wave-equation migration

## Slide 78: The invention of wave-equation migration

## Slide 79: The invention of wave-equation migration

## Slide 80: The invention of wave-equation migration

## Slide 81: The invention of wave-equation migration

## Slide 82: The invention of wave-equation migration

## Slide 83: The invention of wave-equation migration

## Slide 84: The invention of wave-equation migration

## Slide 85: The invention of wave-equation migration
Claerbout, 1971

## Slide 86: Wavefield propagation forwards in time

## Slide 87: Wave propagation and the imaging condition
Here we see a shot point illuminating some reflection points on the sea floor

## Slide 88: Wave propagation and the imaging condition
Rather than imagining this as rays, we can look at the actual wavefield propagating in time.

## Slide 89: Wave propagation and the imaging condition
Is it OK to imagine this as rays?

## Slide 90: Wave propagation and the imaging condition
The shot fires at time zero…

## Slide 91: Wave propagation and the imaging condition
..and we see the Source wavefield forward propagating into the Earth

## Slide 92: Wave propagation and the imaging condition
..and we see the Source wavefield forward propagating into the Earth

## Slide 93: Wave propagation and the imaging condition
The red cone highlights the portion of the Source Wavefield that will be recorded by our receivers.

## Slide 94: Wave propagation and the imaging condition
Raypaths in the red cone: Do they form the wavefield?

## Slide 95: Wave propagation and the imaging condition
As the wavefield hits the seafloor we see some of the wavefield transmitted and some reflected.

## Slide 96: Wave propagation and the imaging condition
As the wavefield hits the seafloor we see some of the wavefield transmitted and some reflected.

## Slide 97: Wave propagation and the imaging condition
As the wavefield hits the seafloor we see some of the wavefield transmitted and some reflected.

## Slide 98: Wave propagation and the imaging condition
As the wavefield hits the seafloor we see some of the wavefield transmitted and some reflected.

## Slide 99: Wave propagation and the imaging condition
This red line shows where the Source wavefield would be if there were no velocity change at the seafloor

## Slide 100: Wave propagation and the imaging condition
This red line shows the portion of the wavefield that will be recorded at our receivers.

## Slide 101: Wave propagation and the imaging condition
We call this upcoming wavefield, which will be recorded at the receivers, the Receiver wavefield.

## Slide 102: Wave propagation and the imaging condition
This location on the seafloor is where the Source Wavefield and the Receiver Wavefield are coincident.

## Slide 103: Wave propagation and the imaging condition
This location on the seafloor is where the Source Wavefield and the Receiver Wavefield are coincident.

## Slide 104: Wave propagation and the imaging condition
This location on the seafloor is where the Source Wavefield and the Receiver Wavefield are coincident.

## Slide 105: Wave propagation and the imaging condition
This location on the seafloor is where the Source Wavefield and the Receiver Wavefield are coincident.

## Slide 106: Wave propagation and the imaging condition
The Source Wavefield and the Receiver Wavefield being coincident is the Imaging condition.

## Slide 107: Wave propagation and the imaging condition
The Source Wavefield and the Receiver Wavefield being coincident is the Imaging condition.

## Slide 108: Wave propagation and the imaging condition
The Source Wavefield and the Receiver Wavefield being coincident is the Imaging condition.

## Slide 109: Wave propagation and the imaging condition
The Source Wavefield and the Receiver Wavefield being coincident is the Imaging condition.

## Slide 110: Wave propagation and the imaging condition
The Source Wavefield and the Receiver Wavefield being coincident is the Imaging condition.

## Slide 111: Wave propagation and the imaging condition
The Source Wavefield and the Receiver Wavefield being coincident is the Imaging condition.

## Slide 112: Wave propagation and the imaging condition
The Source Wavefield and the Receiver Wavefield being coincident is the Imaging condition.

## Slide 113: Wave propagation and the imaging condition
The Source Wavefield and the Receiver Wavefield being coincident is the Imaging condition.

## Slide 114: Wave propagation and the imaging condition
The Source Wavefield and the Receiver Wavefield being coincident is the Imaging condition.

## Slide 115: Wave propagation and the imaging condition
The Source Wavefield and the Receiver Wavefield being coincident is the Imaging condition.

## Slide 116: Wave propagation and the imaging condition
The upcoming Receiver wavefield is now being recorded at the first receiver

## Slide 117: Wave propagation and the imaging condition
We can sometimes (always?) plot the source-reflector-receiver raypath.

## Slide 118: Wave propagation and the imaging condition
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 119: Wave propagation and the imaging condition
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 120: Wave propagation and the imaging condition
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 121: Wave propagation and the imaging condition
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 122: Wave propagation and the imaging condition
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 123: Wave propagation and the imaging condition
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 124: Wave propagation and the imaging condition
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 125: Wave propagation and the imaging condition
t=1.0s-
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 126: Wave propagation and the imaging condition
t=1.0s-
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 127: Wave propagation and the imaging condition
t=1.0s-
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 128: Wave propagation and the imaging condition
t=1.0s-
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 129: Wave propagation and the imaging condition
t=1.0s-
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 130: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 131: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 132: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 133: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 134: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=0.9s-
t=0.8s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 135: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=1.2s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 136: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=1.2s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 137: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=1.2s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 138: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=1.2s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 139: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=1.2s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 140: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 141: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 142: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 143: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 144: Wave propagation and the imaging condition
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 145: Wave propagation and the imaging condition
t=1.4s-
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 146: Wave propagation and the imaging condition
t=1.4s-
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 147: Wave propagation and the imaging condition
t=1.4s-
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.8s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 148: Wave propagation and the imaging condition
t=1.4s-
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 149: Wave propagation and the imaging condition
t=1.4s-
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.9s-
We can plot the Receiver wavefield on our shot gather as it is recorded.

## Slide 150: Wave propagation and the imaging condition
t=1.5s-
t=1.4s-
t=1.0s-
t=1.1s-
t=1.2s-
t=1.3s-
t=0.9s-
Here is the complete seafloor event recorded on our shot gather

## Slide 151: To be continued…