## Slide 1
Standard migration is a combination of
Superposition of wave propagation (correct)
Huygens’ principle, forward and backward in time
Single scatter (superposition of diffraction: Born approximation)
Imaging condition
R = U / D R = U D*
R = U D* / D D*
U = R D
R = U / D
D
U
Theoretically better
Bending the rules: Least-squares migration (LSM)

## Slide 2
Bending the rules: Least-squares migration (LSM)
Standard migration is a combination of
Superposition of wave propagation (correct)
Huygens’ principle, forward and backward in time
Single scatter (superposition of diffraction: Born approximation)
Imaging condition
R = U / D R = U D*
R = U D* / D D*

## Slide 3
Standard migration rules
LSM starts with linearized modeling:
Superposition of wave propagation (correct)
Huygens’ principle, forward and backward in time
Single scatter (superposition of diffraction: Born approximation)
d = L m
Recorded data
Linearized wave operator
“Reflectivity” or perturbation model

## Slide 4
Least-squares migration
LSM starts with linearized modeling:
Superposition of wave propagation (correct)
Huygens’ principle, forward and backward in time
Single scatter (superposition of diffraction: Born approximation):
d = L m
Simply invert for m?
m = L-1 d (e.g., Bleistein et al., 2000)

## Slide 5
Least-squares migration
Two purposes of LSM:
Compensate for acquisition deficiencies
Compensate for subsurface illumination deficiencies

## Slide 6
Least-squares migration
LSM starts with linearized modeling:
Superposition of wave propagation (correct)
Huygens’ principle, forward and backward in time
Single scatter (superposition of diffraction: Born approximation)
d = L m
Simply invert for m?
m = L-1 d
Not so fast! Does L-1 exist? Remember
                surround the obstacle
                continuous time measurements
                continuous spatial grid
                full time / space bandwidth
                perfect subsurface illumination

## Slide 7
Least-squares migration
m = L-1 d
is too ambitious because L-1 does not exist given finite acquisition.
Claerbout recognized that conjugate transpose LH does exist, and that
m = LH d
is the same as imaging condition
R = U D*.

## Slide 8
Least-squares migration
In general, we can’t invert
d = L m.
But we can pseudo-invert (maybe):
LH d = LH L m
m = (LHL)-1 LH d
(if (LHL)-1 exists), which is closer to imaging condition
R = U / D.
We call m = (LHL)-1 LH d least-squares migration.

## Slide 9
Least-squares migration
Even if we can’t pseudo-invert d = L m :
Call mmig = LH d. Then
mmig = (LH L) m,
i.e., migration produces desired reflectivity m, convolved with blurring function LH L.
Can usually deconvolve to get an estimate of m which is sharper than mmig : migration deconvolution (e.g., Hu et al., 2001).
We use the notation = (LHL)-1 LHd even if it isn’t really correct.