## Slide 1: Bramante Staircase (double helix)

## Slide 2: Bramante Staircase and DNA (double helix)

## Slide 3: Flat event response
To calculate a flat event response of a Kirchhoff migration
  Sum over x
  Do it in the frequency domain
  time shift operator d(t+Dt) e i w Dt
  1996 paper
  https://doi.org/10.1190/1.1887374

## Slide 4: Kirchhoff PULL
Foreach image point (x,z)
Output(x,z) = SUMl Input[l,t(x-l,z)]
(x,z) is the image point
SUMl is summation over l
t() is the hyperbola
(vt/2)2 = z2 + (x-l)2
(x,z)
(l,z=0)

## Slide 5: Code (reproduced 2020) —comments
/*
This programs follows this 1996 paper: Dealiasing DMO: Good‐pass, bad‐pass, and unconstrained. Ronen, Nichols, Bale, and Ferber
https://doi.org/10.1190/1.1887374
https://library.seg.org/doi/abs/10.1190/1.1887374
The 1996 paper did it for (Kirchhoff) DMO. This program is for (Kirchhoff) Migration. Post stack or Zero Offset Migration
The idea is to calculate a flat event response.
The program sums over a diffraction hyperbola from a point (x0,z0) to a surface point (x,z=0)
t(t0,x0,x) = sqrt (t0^2 + (2*(x-x0)/v)^2
where t0 = 2/v*z0
In General the Kirchhoff integral would be Image(z0,x0) = integral dx C(x) Data(t(t0,x-x0),x)
Because we calibrate a flat event, we can set x0=0 Image(z) = integral dx C(x) Data(t(t0),x)
t(t0,x) = sqrt (t0^2 + (2*x/v)^2
C() is a an operator which is expected to contain a scalar times a half derivative. What we know about C() is that it contains spherical spreading and a Jacobian because the integration is over the hyperbola and not over the horizontal x. For the Jacobian we need dt/dx
t^2 = t0^2 + (2/v)^2 * x^2
2*t*dt = (2/v)^2 * 2*x*dx
dt/dx = (x/t) * (2/v)^2
dl^2 = dt^2 + dx^2
Jacobian = dl/dx = sqrt(1+(x/t*(2/v)^2)^2)
We can do the above in the frequency domain
Image(kz) = integral dx C(x) exp(i*w*t(t0,x) * Data(w,x)
We expect that if we know C() the results would be
Image(z) = delta(z-z0)
Image(kz) = exp(i*kz*z0)
If we don't know C() then the output would be
Image(kz) = C(kz) * exp(i*kz*z0)
We are not interested in exp(i*kz*z0). Only in C() which is complex. We expect sqrt(iw)
*/

## Slide 6: Code—before the integration
int main(int ac, char **av)
{
int i, verbose=1, nx=10001;
double f; FGETPAR(1,f,40.0);
double t0; FGETPAR(2,t0,1.0);
double xmax; FGETPAR(3,xmax,12000.0);
int halfdiff; IGETPAR(4,halfdiff,0);
double xmin = 0.0; double v = 1500.0; double dx = (xmax-xmin)/(nx-1);
double w = 2*M_PI*f; // M_PI is defined by <math.h>
double vh = v/2.0; double ovh = 1.0/vh; double z0 = t0*vh; double t0t0 = t0*t0;
if(verbose) {
if(ac==1) fprintf(stderr, "Example:\n%s [freq_in_Hz t0_in_secs xmax halfdiff]\n",av[0]); // Selfdoc
fprintf(stderr,"f=%g w=%g v=%g t0=%g z0=%g nx=%d xmin=%g xmax=%g dx=%g\n",
f,w,v,t0,z0,nx,xmin,xmax,dx);
}
double re = 0.0;
double im = 0.0;
printf("%g %g\n",re,im); // We want the starting point

## Slide 7: Code—loop over x
82 for(i=0;i<nx;i++) {
83 double x = xmin + i*dx;
84 double xovh = x/vh;
85 double t = sqrt(t0t0 + xovh*xovh);
86 double jac = sqrt(1.0+xovh*xovh/t/t);
87 double dre = cos(w*(t-t0));
88 double dim = sin(w*(t-t0));
89 if(i==0) { dre *= 0.5; dim *= 0.5; } // We are summing only on positive x
90
91 // Jacobian: Integral dl = jac * dx
92 dre *= jac*dx;
93 dim *= jac*dx;
94
95 // Spherical spreading 1/sqrt(time) in 2D
96 dre /= sqrt(t);
97 dim /= sqrt(t);
98
99 re += dre;
100 im += dim;
101
102 if(halfdiff) printf("%g %g\n",(re+im)*sqrt(w/2),(im-re)*sqrt(w/2));
103 else printf("%g %g\n",re,im);
104 }

## Slide 8: Results—4km aperture, t0=1 seconds
Observations
Low frequency: slow convergence
Half integral
  Low frequencies scaled up
  All frequencies converge to points almost exactly on the sqrt(i) line  45 degree phase
  There is a factor 2 scale in amplitude for every factor 4 in frequency  sqrt(w)
  Hence: 1/sqrt(iw)  half integral!
  we need a Half derivative to prevent the half integral
5 Hz
20 Hz
80 Hz

## Slide 9: Results—4km aperture, t0=4 seconds
Observations
Almost exactly as t0=1
There is a dependency on frequency but not on t0
5 Hz
20 Hz
80 Hz

## Slide 10: Results with half derivative option on, t0=1
5 Hz
20 Hz
80 Hz
Observations
They all converge to about the same point more or less on the real axis
Slightly off
It’s not roundoff errors because single precision and double precision give the same results
I don’t know why it’s slightly off

## Slide 11: Results with half derivative option on, t0=4
Observations
They all converge to about the same point more or less on the real axis: (950,0)
Less off than t0=1 because of roundoff errors? (we did it in double)
I don’t know what to normalize by to make (950,0) to (1,0). nx=10001 in these runs
5 Hz
20 Hz
80 Hz

## Slide 12: Low frequency imaging
Velocity model building such as FWI benefits from low frequencies signal
  Avoiding local minima (“cycle skips”) in fitting the data
Imaging low frequencies should also benefit
  Sub-salt/Sub-basalt/Blocky reservoir model building
But it seems like Imaging has a low frequency limitation
  In Kirchhoff there is a stationary phase approximation and a zero divided by zero implied by correcting/pre-empting a half integral by a half derivative: sqrt(iw) / (1/sqrt(iw)
  FK and FD migration methods may have a problem with very low frequencies for any reflector that is not flat w/k>Vmin

## Slide 13: Spiral plots for Ultra Low Frequency
With maximal offset of 4km they do not converge at 0.5 Hz
With up to 4 km offset, we will not be able to image 1Hz and below even if we we have a 1Hz source

## Slide 14: Spiral plots for Ultra Low Frequency
With maximal offset of 40km they converge
We can image 0.5 Hz signal if
  we had 0.5 Hz sources and receivers
  Ultra Long Offset

## Slide 15: tpow=1
Observations
Slightly faster convergence
5 Hz
20 Hz
80 Hz

## Slide 16: Default: tpow=0.5
Observations
This is the same as two of the previous slides
5 Hz
20 Hz
80 Hz

## Slide 17: tpow=0
Observations
Slightly slower convergence
5 Hz
20 Hz
80 Hz

## Slide 18: tpow=-1
Observations
Slower convergence
But it still converges—at least down to 5 Hz
5 Hz
20 Hz
80 Hz

## Slide 19: tpow=-4
Observations
Low frequency does not converge
High frequencies converge slower
5 Hz
20 Hz
80 Hz

## Slide 20: Snails and Spirals
Other snails
  Airgun signature and Mie scattering
  Ghosting operator
  Airgun energy cross-plot

## Slide 21: Airgun signature and spectrum
Time Domain Frequency Domain (log-log)

## Slide 22: Mie scattering
Time Domain Frequency Domain (log-log)
http://en.wikipedia.org/wiki/Mie_scattering
The Mie solution toMaxwell’s equations describes the scattering of an EM wave by a homogeneous sphere.
It is named after Gustav Mie. (1868-1957)

## Slide 23: Mie scattering (frequency domain log-log)
Radar Cross Section (RCS) is the ability of an airplane to reflect radar
Also reflection of light/IR from air molecule:
  blue sky, red sunset
Very Low frequency: λ >> size: RCS = 0
Rayleigh scattering: λ > size: RCS ~ λ-4
Mie scattering: λ ≈ size: RCS = resonantive
High frequency: λ<<size : RCS = size2

## Slide 24: Mie scattering (frequency domain log-log)
Radar Cross Section (RCS) is the ability of an airplane to reflect radar
Also reflection of light/IR from air molecule:
  blue sky, red sunset
Very Low frequency: λ >> size: RCS = 0
Rayleigh scattering: λ > size: RCS ~ λ-4
Mie scattering: λ ≈ size: RCS = resonantive
High frequency: λ<<size : RCS = size2

## Slide 25: Mie scattering (frequency domain log-log)
Radar Cross Section (RCS) is the ability of an airplane to reflect radar
Also reflection of light/IR from air molecule:
  blue sky, red sunset
Very Low frequency: λ >> size: RCS = 0
Rayleigh scattering: λ > size: RCS ~ λ-4
Mie scattering: λ ≈ size: RCS = resonantive
High frequency: λ<<size : RCS = size2

## Slide 26: Mie scattering (frequency domain log-log)
Radar Cross Section (RCS) is the ability of an airplane to reflect radar
Also reflection of light/IR from air molecule:
  blue sky, red sunset
Very Low frequency: λ >> size: RCS = 0
Rayleigh scattering: λ > size: RCS ~ λ-4
Mie scattering: λ ≈ size: RCS = resonantive
High frequency: λ<<size : RCS = size2

## Slide 27: Mie scattering (frequency domain log-log)
Radar Cross Section (RCS) is the ability of an airplane to reflect radar
Also reflection of light/IR from air molecule:
  blue sky, red sunset
Very Low frequency: λ >> size: RCS = 0
Rayleigh scattering: λ > size: RCS ~ λ-4
Mie scattering: λ ≈ size: RCS = resonantive
High frequency: λ<<size : RCS = size2

## Slide 28: Mie scattering (frequency domain log-log)
Complex Hodogram
Real
Imaginary
?
(0,0) (1,0)
Frequency = almost 0 (very small)
Frequency = almost Infinity (very high)
Radar Cross Section (RCS) is the ability of an airplane to reflect radar
Also reflection of light/IR from air molecule:
  blue sky, red sunset
Very Low frequency: λ >> size: RCS = 0
Rayleigh scattering: λ > size: RCS ~ λ-4
Mie scattering: λ ≈ size: RCS = resonantive
High frequency: λ<<size : RCS = size2

## Slide 29: Mie Scattering and Airgun signature spectra
Similar

## Slide 30: Mie spectra and Airgun spectra and hodograms
They spiral!

## Slide 31: Mie spectra and Airgun spectra and hodograms
The difference in the high frequencies is because the force of the air coming out of an airgun is band-limited

## Slide 32: Mie spectra and Airgun spectra and hodograms
They are not only minimum phase.
They are (pretty much) positive real!

## Slide 33: Positive Real (PR) and Minimum Phase (MP)
Every Positive Real is also Minimum Phase
The convolution of any two MP’s is MP
The convolution of any two PR’s is MP, but (usually) not PR
  because (x1+iy1)(x2+iy2)=(x1x2-y1y2) + i(x1y2+y1x2)
The sum of any PR’s is PR (and MP)
  because (x1+iy1)+(x2+iy2) = (x1+x2) + i(y1+y2)
  S Positive Real = Positive Real

## Slide 34: The Significance of ΣPR = Positive Real
The signature of an Airgun array is the sum of the signatures of each
If each gun is PR and if they all go off at the same time then the sum is PR
If they don’t go off at the same time then it will be neither PR nor even MP ! Not good (?)
If each gun is MP but not PR, then in general, their sum will not be MP

## Slide 35: Airgun arrays, including their ghosts
Any PR wavelet is MP
The sum of PR wavelets is PR
  So a heterogeneous Airgun array is PR (and MP)
  The ghosts are like another array above the sea surface
  So is a ghosted airgun array PR?
No, because the ghosts have a time delay
  Ghosting is a convolution and not summing
  Convolution of two positive real wavelets is not positive real
  Convolution of two minimum phase wavelets is minimum phase
Let’s look at a ghosted airgun signature

## Slide 36: The Ghosted airgun is not positive real
Airgun
Ghosted
Airgun

## Slide 37: Snails and Spirals
Other snails
  Airgun signature and Mie scattering
  Ghosting operator
  Airgun energy cross-plot

## Slide 38: Focus on the source ghost
Time domain
  G(t) = d(t) – R d(t-tg)
Frequency domain
  G(w) = 1 – R eiwtg
Z Transform
  Delay operator Z = eiw
  G(Z) = 1 – R Ztg
Source
Ghost Source
Time delay tg = 2d cos q / v
For example, if d=7.5m,
q=0, and v=1500m/s
then tg= 10 msec
d
Ghost Rd(t-tg)
Primary d(t)
q
R

## Slide 39: Ghosting operator: Primary + Ghost
Time domain
  G(t) = d(t) – R d(t-tg)
Frequency domain
  G(w) = 1 – R e iwtg
Z Transform Z = eiw
  G(Z) = 1 – R Z tg
R=1

## Slide 40: Ghosting operator: Primary + Ghost
Time domain
  G(t) = d(t) – R d(t-tg)
Frequency domain
  G(w) = 1 – R e iwtg
Z Transform Z = eiw
  G(Z) = 1 – R Z tg
R=1
Abs
Real
Imag
Cross plot of Real vs Imag
(Complex plane)
1
1-R e iwtg
1-R e i(w+dw)tg
0 1 2

## Slide 41: Ghosting operator: Primary + Ghost
Time domain
  G(t) = d(t) – R d(t-tg)
Frequency domain
  G(w) = 1 – R e iwtg
Z Transform Z = eiw
  G(Z) = 1 – R Z tg
Unit circle in the Z complex plane
No Poles
tg zeroes
  Whenever 1 = R Z tg
  On the unit circle with R = 1
  Outside the circle when R<1 (much nicer)
0
0
0
0
0
0
0
0
0
0
R=1
-1 0 1

## Slide 42: Frequency dependent R(w) or R(Z) < 1
Acoustics: 0.9994
Spherical spreading
Swell
Visco-acoustics
Two different things
  Both frequency dependent
  Swell factor is weather dependent
  Visco-acoustic depends on source depth
Source
R
Seabed
Air
Water
Target Reflectors
RR(Z)

## Slide 43: G(Z) = 1 – R(Z) Z tg ; R(Z) = Red Ghost
R = 1
R(Z)
Time domain Impulse Responses
Frequency domain Real-Imaginary cross plots
Causal
Positive Real hence Minimum Phase

## Slide 44: Snails and Spirals
Other snails
  Airgun signature and Mie scattering
  Ghosting operator
  Airgun energy cross-plot

## Slide 45: Physics of Air Guns and Sources in general
Radiating oscillators (Rayleigh’s equation)
Far field. Applies to sources in general (not only air guns but also vibes)
R = bubble radius; V = source volume; p = pressure; r = distance to receiver; ∞ = water
Ideal Gas equation
  PV = nRT
Adiabata equation
PVg = Constant
g = 1.4
Temperature changes
k (PV)1/3
(10+Depth) 5/6
Rayleigh-Willis formula
Tb =

## Slide 46: Integrate the far field signature twice
Far field Pressure
Bubble Volume
d2/dt2
Frequency2
Integrate twice
SSdt2
1/Frequency2

## Slide 47: Integrate the far field signature twice
Far field Pressure
Bubble Volume


Very soon (<miliscond) after the shot is triggered the ports are open and a small high pressure bubble is formed

## Slide 48: Integrate the far field signature twice
Far field Pressure
Bubble Volume


The bubble is expanding, the pressure inside it is dropping and soon (10-20 milisconds) it reaches ambient pessure

## Slide 49: Integrate the far field signature twice
Far field Pressure
Bubble Volume


The bubble continues to expand but slowing. 60 milisconds later it reaches maximal volume and minimal pressure

## Slide 50: Integrate the far field signature twice
Far field Pressure
Bubble Volume

6 m3 are displaced when the bubble is at maximal size and the pressure inside it is minimal


## Slide 51: Integrate the far field signature twice
Far field Pressure
Bubble Volume


Ambient pressure again

## Slide 52: Integrate the far field signature twice
Far field Pressure
Bubble Volume


First bubble collapse (here 220 msec bubble period
… etc.

## Slide 53: Bubble radius calculated from the volume
Bubble Radius
Bubble Radius Velocity
Bubble Radius Acceleration
Volume = 4p/3 R3

## Slide 54: Cross-plot Radius and velocity
Bubble Radius
Bubble Radius Velocity
Notes: Harmonic oscillator constant energy = ½ kx^2 + ½ mv^2

## Slide 55: Energy crossplot
Bubble Temperature
Potential Energy (gravity)

## Slide 56: Energy crossplot
Bubble Temperature
Potential Energy (gravity)
Kinetic Energy

## Slide 57: Energy crossplot
Bubble Temperature
Potential Energy (gravity)
Kinetic Energy
Potential Energy (elastic)

## Slide 58: Energy crossplot
Bubble Temperature
Potential Energy (gravity)
Kinetic Energy
Potential Energy (elastic)

## Slide 59: Radiating adiabatic oscillator
Bubble Temperature
Energy:
Kinetic proportional to Velocity2
Potential proportional to (R-R∞) 2
Thermal proportional to Temperature
Radiated acoustic wave Energy
Some wasted on turbulence

## Slide 60: Radiating adiabatic oscillator
Bubble Temperature
Energy:
Kinetic proportional to Velocity2
Potential proportional to (R-R∞) 2
Thermal proportional to Temperature
Radiated acoustic wave Energy
Some wasted on turbulence
Potential Energy
Kinetic Energy
R-R∞
Velocity dR/dt
Mechanical Energy

## Slide 61: Zero velocity so zero Kinetic Energy
Bubble Temperature maxima
Energy:
Kinetic proportional to Velocity2
Potential proportional to (R-R∞) 2
Thermal proportional to Temperature
Radiated as acoustic wave










0
0
1
1
2
2
3
3
4
4

## Slide 62: Zero Kinetic Energy
Bubble Temperature minima
Energy:
Kinetic proportional to Velocity2
Potential proportional to (R-R∞) 2
Thermal proportional to Temperature
Radiated as acoustic wave










5
1
2
3
4
5
1
2
3
4

## Slide 63: R=R∞ Zero Potential Energy
Bubble Temperature
Bubble Pressure = ambient pressure










5
1
5
1

## Slide 64: Zero Potential Energy
Bubble Temperature
Bubble Pressure










5
1
1
5